## Slide 1: Silicon Hydride Safe Handling
Self Auditing Tool
March 2022
Notes: Thank you for your interest in the safe handling of silicon hydrides. I’m Bill Maki with over 37 years of experience in the silicone industry. On the behalf of the Silicones Environmental, Health, and Safety Center of the ACC, I will be introducing a self auditing tool for the safe handling of silicon hydride safe.

## Slide 2: Introduction
This presentation and audit tool was developed by Jeff Gray and Bill Maki for and in conjunction with the Silicones Environmental, Health, and Safety Center of the American Chemistry Council.
The information herein is offered in good faith and is believed to be accurate and reliable as of the date of publication; however, it is offered without warranty, expressed or implied, as to merchantability, fitness for a particular purpose, and or any other matter. ACC SEHSC, CES, SIAJ, nor any member company assumes any liability or responsibility for any use, or the results of such use, of the information presented.
Notes: This presentation and audit tool was developed by Jeff Gray and myself for and in conjunction with the SEHSC.
The information herein is offered in good faith and is believed to be accurate and reliable as of the date of publication; however, it is offered without warranty, expressed or implied, as to merchantability, fitness for a particular purpose, and or any other matter. ACC SEHSC, CES, SIAJ, nor any member company assumes any liability or responsibility for any use, or the results of such use, of the information presented.
With the legality behind us, let’s move on with the presentation.

## Slide 3: During this presentation you will learn about the following:
Important reasons to audit a process that handles silicon hydride material
What is silicon hydride
The potential hazards associated with silicon hydride
Available resources to aid in the safe design and operation of a process handling silicon hydride material
An audit tool to aid in auditing a process handling silicon hydride material
Notes: The primary goal of this presentation is to encourage the use of the self audit tool for any processing or handling of a material containing silicon hydride.
In doing so, the following shared learnings will be discussed.
First of all and of upmost importance, why is it important to audit a process that uses a silicon hydride material. Let’s face it, in today’s busy work environment, if there is not a sound reason for prioritization, it won’t get done.
Next, a quick discussion on what a silicon hydride material is.
Followed by the potential hazards of silicon hydride materials.
A review of the available resources to aid in the design and operation of a process handling a silicon hydride material.
Then wrapping up with a discussion on the self auditing tool.

## Slide 4: Why Audit?
To help prevent repeat of past industry fires and explosions while handling silicon hydride materials
Example: Explosion due to improperly handled silicon hydride material investigated by the CSB
  AB Specialty Silicones
  May 2019
  Explosion and fire
  Four workers fatally injured
Notes: So, why audit?
There is a history of fires and explosions in industry during the processing and handling of silicon hydride materials . Many of these incidents result in injuries, property damage and lost production.
A recent example is the explosion that occurred at AB Specialty Silicones in May 2019. An unexpected release of hydrogen from a silicon hydride material into the building caused an explosion and fire. This resulted in the death of four workers and the destruction of a production building.
The impact on the site and community can be seen in the picture and the news video.
PLAY VIDEO
The Chemical Safety Board investigated this incident and published their findings and recommendation in a report on their website. The report is done very well and should be reviewed with your safety, engineering and manufacturing departments.
So back to auditing. Auditing is a critical tool that we can use to aid in training and identify gaps in the manufacturing process in order to reduce the incidents and impact of silicon hydrides.

## Slide 5: What is a Silicon Hydride?
Simply put…a Si-H bond
Hydrogen functional silicon compounds may be in the form of silanes, siloxanes and silicones
Silicon hydride example, tetramethyldisiloxane
H O H
Si Si
Notes: What is a silicon hydride?
A silicon hydride is any silicon compound that has a Si-H bond.
These silicon compounds can be in the form of a monomer or polymer. A silane monomer, which is just one silicon, can have one to four Si-H bonds as a silicon hydride.
Siloxanes and silicones are polymers that can have Si-H bonds along the backbone and/or at the terminal ends.
Tetramethyldisiloxane is an example of a silicon hydride material. It has a Si-H bond on each silicon. A key use of tetramethyldisiloxane is to add terminal Si-H bonds to a polymer.

## Slide 6: Silicon Hydride Hazards
SiH functional materials can have a range of general hazards
  Combustible to flammable to pyrophoric
  Non-static accumulating to static accumulating
  Non-corrosive to corrosive
  Non-toxic to toxic
It is important to understand these hazards via the SDS
Notes: Let’s discuss the hazards of silicon hydride materials.
Before discussing the hazards specifically associated to the silicon hydride, it is also important to appreciate the other hazards the material can have.
Because of the broad range of silicon materials that contain silicon hydride, they also have a broad range of other hazards. They can be combustible to flammable liquids and gasses, to pyrophoric. Some are static accumulating, while others are not. You can have corrosive or non-corrosive materials. They can also have a range of toxicity.
Because of this, it is very important to understand these other hazards by carefully reading the safety data sheet.

## Slide 7: Silicon Hydride Hazards
All SiH materials have additional hazards that are important to understand in order to safely handle and process.
SiH will react with an active hydrogen source, such as water and alcohols, to form hydrogen. There are many substances, such as strong acids and bases, that can act as catalysts to increase the rate of hydrogen generation. This can lead to a flammable and/or explosive environment in the building, equipment or container.
Notes: Now that we understand that silicon hydride materials can have many hazards, let’s focus on the ones related to the Si-H bond.
Unlike the stable C-H bond, the Si-H bond is reactive.
Silicon hydride will react with an active hydrogen source, such as water and alcohols, to form hydrogen. The reaction with water and alcohols alone is generally slow. Visually this would look like CO2 bubbles rising from a somewhat flat soda.
The reaction to form hydrogen will become more rigorous if catalysts are added to the mix. Acids and bases are common catalysts causing incidents with silicon hydrides.
Acids will increase hydrogen generation similar to what is seen with CO2 bubbles rising from a freshly poured soda.
A base on the other hand becomes very violent, similar to adding Mementos to soda. In this situation equipment and containers can quickly become over pressurized.
There are many catalysts that can enhance the reaction to form hydrogen. It is very important to understand the relationship between the silicon hydride material and other chemicals that are intentionally mixed or may unintentionally be mixed at the site through reactive chemistry studies.
In all of these cases the hydrogen generated can lead to a fire and/or explosion.

## Slide 8: Silicon Hydride Hazards
Thermal Degradation can cause hydrogen generation, leading to equipment failure, fire and/or explosion. Overheating in a deadheaded centrifugal pump is an example of this type of situation.
SiH is commonly used in hydrosilylation chemistry with catalytic ingredients to accelerate the reaction. This is a very exothermic reaction. If left unchecked, a runaway reaction can generate temperatures and pressures exceeding equipment design, leading to equipment failure, fire and/or explosion.
Notes: Silicon hydride materials can undergo thermal degradation. Degradation can generate hydrogen, leading to equipment failure, fire and/or explosion.
It is important to understand the temperature of degradation in order to design manufacturing processes correctly. A deadheaded centrifugal pump is an example of a situation that can lead to thermal degradation.
Silicon hydride materials are commonly used in hydrosilylation chemistry. This reaction is exothermic in the general range of 33 kcal/gmole.
Temperature control is critical in preventing a runaway reaction. If left unchecked, generated temperatures and pressures can exceed equipment design, leading to equipment failure, fire and/or explosion.

## Slide 9: Silicon Hydride Hazards
SiH materials can rearrange at high temperatures and/or in the presence of a catalyst to form flammable materials.
Some SiH materials can form shock sensitive gels that will generate a fire and/or explosion when disturbed, such as during maintenance operations.
Notes: Silicon hydride materials can rearrange at high temperature and/or in the presence of catalysts to form flammable materials.
It is important to understand the impact of temperature excursions in the manufacturing process through reactive chemistry studies.
Silicon hydride materials, especially chlorosilane containing, can form shock sensitive gels that will generate a fire and/or explosion when disturbed.
The formation of these gels typically occurs as material leaks from the process or water leaks into the process. Extreme caution and a prepared procedure should be used when handling silicon hydride based gels.

## Slide 10: Silicon Hydride Safe Handling Resources
"Materials Handling Guide: Hydrogen-Bonded Silicon Compounds" developed by the Operating Safety Committee of the Silicones Environmental, Health, and Safety Center North America (SEHSC), CES-Silicones Europe (CES), in partnership with the Silicones Industry Association of Japan (SIAJ), July 2016
Notes: The Silicones Environmental, Health and Safety Center has developed the “Materials Handling Guide: Hydrogen-Bonded Silicon Compounds” specifically for individuals and companies handling silicon hydride materials.
This guide is an excellent resource in developing training curriculum, designing manufacturing processes and operating manufacturing processes involving silicon hydride materials.
This guide was used as a reference in the development of this presentation and the audit tool.

## Slide 11: Silicon Hydride Safe Handling Resources
"Safe handling of silicon hydride containing polysiloxanes", The Dow Chemical Company, Form No. 24-711-01-1120 S2D
"Silane Safety/Lessons Learned and Accident Prevention", Air Products
ASTM Manual MNL33, "Chlorosilane Emergency Response Guidelines, 2nd edition" 2014
"Global Safe Handling of Chlorosilanes", Global Silicones Council, 2017 edition
Notes: Here are some additional resources that may be helpful for you in reviewing your silicon hydride handling and processing.

## Slide 12: Audit Tool
  Introduction
  Incidents
  References
  PSM Elements
  Hazard Control
  PPE (Personal Protective
  Equipment)
  Training & Job Safety
  Waste Management
  Emergency Response
  Containers & Shipping
An audit tool using Microsoft Excel has been developed to aid in the safe handling and processing of silicon hydrides.
The audit tool can be found at AmericanChemistry.com/SIH-Audit-Tool.
The audit tool contains the following worksheet tabs.
Notes: With that background, let’s talk about the audit tool.
The audit tool is documented in a Microsoft Excel workbook.
The audit tool is available at address. You may want to pause this presentation and pull up the tool while we continue with the presentation.
In the workbook there is a worksheet tab for the following areas: Introduction, Incidents, References, PSM Elements, Hazard Control, PPE, Training and Job Safety, Waste Management, Emergency Response and Containers and Shipping.
We will discuss each of these tabs in more detail in the following slides.

## Slide 13: Audit Tool
At the top of each audit tab is a section to identify participants, date and background on what is being audited.
There should be more than one participant and participants may vary based on the tab topic.
There are 125 questions in total.
Some questions may not be pertinent to your operation, if so, the review group should make the decision to skip the question(s).
Notes: Before going into the details of each tab, let’s discuss the audit tool in general.
At the top of each audit tab is a section to identify the participants, date and background on what is being audited.
There should be more than one participant when doing the audit. Depending on the topic of the audit tab there may be different participants involved with the audit.
There are a total of 125 questions. Some of these questions may not pertain to your operation. If this is the case, the decision to skip the question should be done by the group.

## Slide 14: Audit Tool – Introduction, Incidents and References
These tabs provide background information on the basis of the audit tool.
It is important for the audit participants to be familiar with this information and any other recognized and generally accepted good engineering practices pertinent to their process.
The audit participants should be familiar with the incidents and how they may apply to their process.
Notes: The Introduction, Incidents and References tabs provide background for the audit tool.
The audit participants should be familiar with this background information and any other recognized and generally accepted good engineering practices that may pertain to their process.
The information on the Incidents tab is especially important. It provides basic information on incidents that have occurred across the silicones industry. This should be used as food for thought as you audit your operations.

## Slide 15: Audit Tool – PSM Elements Tab
A strong Process Safety Management (PSM) system is important for handling and processing silicon hydrides. OSHA PSM is a format that should be considered.
This tab has 23 questions.
E.g. – Has a Process Hazard Analysis been completed?
Notes: The first audit tab pertains to OSHA PSM.
Due to the safety hazards associated with silicon hydrides, a strong Process Safety Management system is imperative. Even if your process does not meet the regulatory requirements for OSHA PSM, it is strongly recommended to use PSM for your process.
There are 23 questions on this tab. At a minimum a manufacturing representative and safety representative should conduct this portion of the audit.
An example question is – Has a process hazard analysis been completed?

## Slide 16: Audit Tool – Hazard Control and PPE Tab
These tabs review procedural and engineering controls when handling and processing silicon hydrides.
The Hazard Control tab has 55 questions.
E.g. – Are hydrogen monitors in use?
The PPE tab has 6 questions.
E.g. – Was a flash fire due to hydrogen considered when selecting the appropriate PPE?
Notes: The Hazard Control and PPE tabs cover procedural and engineering controls.
The hazard control tab has 55 questions. At a minimum a manufacturing representative, safety representative and engineering representative should conduct this portion of the audit.
An example question is – Are hydrogen monitors in use?
There are 6 questions on the PPE tab. At a minimum a manufacturing representative, safety representative and industrial hygiene representative should conduct this portion of the audit.
An example question is – Was a flash fire due to hydrogen considered when selecting the appropriate PPE?

## Slide 17: Audit Tool – Training & Job Safety Tab
Employee training is the first line of defense in a strong safety program.
The Training & Job Safety tab reviews key information that should be available to employees who handle silicon hydrides and on which they should be trained.
This tab has 11 questions.
E.g. – Does the SOP have a safety key point on building evacuation due to abnormal
operating conditions?
Notes: The next tab covers training and job safety.
Employee training is the first line of defense in a strong safety program. There are a lot of nuances in handling silicon hydrides and providing the appropriate training will aid employees in identifying an issue before it becomes an incident.
This tab has 11 questions. At a minimum an operator, manufacturing representative and safety representative should conduct this portion of the audit.
An example question is – Does the SOP have a safety key point on building evacuation due to abnormal operating conditions?

## Slide 18: Audit Tool – Waste Management Tab
A key hazard for silicon hydrides is the mixing of incompatible materials.
The Waste Management tab focuses on ways to prevent the mixing of incompatible waste materials and sharing of silicon hydride hazards with the off-site waste handlers.
This tab has 6 questions.
E.g. – Are there procedures in place to maintain separation between SiH waste and other waste
to prevent undesired reactions?
Notes: The audit tool has a waste management tab.
Sometimes waste management can be overlooked. Due to the hazards of mixing incompatible materials with silicon hydrides it becomes a very important area to audit, not only in regards to internal operations, but also the information and training shared with the off-site waste handlers.
This becomes especially alarming when a waste gets unintentionally mixed with a silicon hydride containing waste. Appropriate waste segregation is a necessity when silicon hydrides are involved.
This tab has 8 questions. At a minimum a manufacturing representative, safety representative and environmental representative should conduct this portion of the audit.
An example question is – Are there procedures in place to maintain separation between SiH waste and other waste to prevent undesired reactions?

## Slide 19: Audit Tool – Emergency Response Tab
Because of the potential for hydrogen during an emergency it is important to have vetted emergency response plans in place to train employees before an event.
This tab has 8 questions.
E.g. – Does the ERP include procedures on how to handle bulged (over-pressurized) drums and/or IBC's?
Notes: The next tab covers the Emergency Response Plan for the site.
Because of the potential for hydrogen during an emergency it is important to have a vetted emergency response plan in place to train employees before an event. Your local fire department should also be aware that you are handling silicon hydrides and the appropriate actions to take in the event of an incident.
The Emergency Response tab has 8 questions. At a minimum a manufacturing representative and safety representative should conduct this portion of the audit.
An example question is – Does the emergency response plan include procedures on how to handle bulged (over-pressurized) drums and/or IBC’s?

## Slide 20: Audit Tool – Containers & Shipping Tab
Packaging and shipping of silicon hydrides generally call for special consideration. This tab focuses on this aspect of handling.
This tab has 16 questions.
E.g. – Are drums and IBC's fitted with a vented bunge?
Notes: The last tab covers Containers and Shipping.
Packaging and shipping of silicon hydrides call for special consideration to prevent an incident from happening at your site, but also at your customer’s site.
This tab has 16 questions. At a minimum a manufacturing representative, safety representative and shipping/transportation representative should conduct this portion of the audit.
An example question is – Are drums and IBC’s fitted with a vented bunge?

## Slide 21: Contact Information
SEHSC
AmericanChemistry.com/SIH-Audit-Tool
Betsy Beckwith – betsy_beckwith@americanchemistry.com
Jeff Gray – jag6691@gmail.com
Bill Maki – williammaki@charter.net
Notes: Thank you for your interest in the safe handling of silicon hydrides.
This presentation and the audit tool can be found on the address.
If you have any questions, please feel free to contact Betsy Beckwith at the ACC or Jeff Gray and myself.
Again, thankyou for allowing us to share this information with you in the hope to make your process handling silicon hydride safer.